## Slide 1: Lab 2: FIR Filter Implementation using a Linear and Circular buffer
EE 462 – DSP Lab

## Slide 2: Linear Convolution in real-time
Linear buffer: For every output sample y[n], we read in one input sample x[n] and shifted the previous input samples in the linear buffer by one place =>
we used N (= length of i.r.) read/write operations
The above can be eliminated by using a “circular buffer”, i.e. dedicated hardware that helps achieve only a single write operation per output sample.
A circular buffer is specified by its start address, length and increment size.

## Slide 3: Lab Objectives
Configure the DSP hardware to use linear or circular buffer.
Implement convolution using linear or circular buffer.
Compare the performance of the linear and circular buffer implementation using profiling

## Slide 4: How to do in real time ?
Real time:
Continuous stream of input samples (cannot store all the samples in memory).
Realtime Implementation:
  Linear Buffer.
  Circular Buffer
Y[0]=h[0]*x[0] + h[1]*x[-1] + h[2]*x[-2] + h[3]*x[-3]
Y[1]=h[0]*x[1] + h[1]*x[ 0] + h[2]*x[-1] + h[3]*x[-2]
Y[2]=h[0]*x[2] + h[1]*x[ 1] + h[2]*x[ 0] + h[3]*x[-1]
Y[3]=h[0]*x[3] + h[1]*x[ 2] + h[2]*x[ 1] + h[3]*x[ 0]
Filter length : 4

## Slide 5: Circular Buffer
0 | 0 | 0 | 0
Define input buffer of same length as that of the filter. Pointer to circular buffer points to first element.

## Slide 6
X[0] | 0 | 0 | 0
Once the input is stored, pointer will be incremented and will point to next location.
Circular Buffer

## Slide 7
X[0] | 0 | 0 | 0
X[0] | X[1] | 0 | 0
Once the input is stored, pointer will be incremented and will point to next location.
Circular Buffer

## Slide 8: Circular Buffer
X[0] | 0 | 0 | 0
X[0] | X[1] | 0 | 0
X[0] | X[1] | X[2] | 0
Once the input is stored, pointer will be incremented and will point to next location.

## Slide 9: Circular Buffer
X[0] | 0 | 0 | 0
X[0] | X[1] | 0 | 0
X[0] | X[1] | X[2] | 0
X[0] | X[1] | X[2] | X[3]
Once the input is stored, pointer will be incremented, since the buffer is configured as circular buffer, the pointer will wrap around and point to first location.

## Slide 10: Circular Buffer
X[0] | 0 | 0 | 0
X[0] | X[1] | 0 | 0
X[0] | X[1] | X[2] | 0
X[0] | X[1] | X[2] | X[3]
X[4] | X[1] | X[2] | X[3]
Once the input is stored, pointer will be incremented and will point to next location.

## Slide 11: Circular Buffer
X[0] | 0 | 0 | 0
X[0] | X[1] | 0 | 0
X[0] | X[1] | X[2] | 0
X[0] | X[1] | X[2] | X[3]
X[4] | X[1] | X[2] | X[3]
X[4] | X[5] | X[2] | X[3]
Once the input is stored, pointer will be incremented and will point to next location.

## Slide 12: Convolution
X[4]
X[5]
X[2]
X[3]
h[0]
h[1]
h[2]
h[3]
X[4]
X[5]
X[2]
X[3]
h[0]
h[1]
h[2]
h[3]
Decrement pointer of circular buffer for alignment and multiply corresponding element for convolution by decreasing circular buffer pointer and increasing coefficient buffer pointer.
Y[5]=h[0]*x[5] + h[1]*x[4] + h[2]*x[3] + h[3]*x[2]

## Slide 13: Convolution
X[4]
X[5]
X[2]
X[3]
h[0]
h[1]
h[2]
h[3]
X[4]
X[5]
X[2]
X[3]
h[0]
h[1]
h[2]
h[3]
Decrement pointer of circular buffer for alignment and multiply corresponding element for convolution by decreasing circular buffer pointer and increasing coefficient buffer pointer.
Y[5]=h[0]*x[5] + h[1]*x[4] + h[2]*x[3] + h[3]*x[2]

## Slide 14: Assembly code Syntax

## Slide 15: Thank You